## Slide 1: WindTrue: Workshop on sensitivity analysis using UQLab
CWI Amsterdam
Jan 13, 2020
Prashant Kumar
Benjamin Sanderse
Vinit Dighe

## Slide 2: Workflow

## Slide 3: Background material
User manual of our workflow: on Git repository.
UQLab examples and user manual: https://www.uqlab.com/

## Slide 4: Installation
Clone from the git repository
Modify “config.m” file that stores path to your UQLab installation
  For e.g., UQLab_path = ‘C:\User\UQLab\’
Go to the directory ‘\windtrue\sensitivity_analysis\cases\Ishigami’ and run ‘UQLab_simple_test’ from Matlab command window

## Slide 5: Part I Theory and UQLab intro

## Slide 6: Propagation
Inflow conditions
BEM parameters
Blade geometry
...
Power
Fatigue loads
Moments
…

## Slide 7: Propagation

## Slide 8: Monte Carlo
slow convergence
random samples qi
with equal weights

## Slide 9: Surrogate models
Full model response
Response surface
Polynomials
Radial basis functions
Gaussian processes
Neural networks

## Slide 10: Sensitivity analysis
Global sensitivity analysis
Decompose variance of output in terms of variance of inputs
Sobol’ indices (first order)

## Slide 11: UQLab

## Slide 12: UQLab

## Slide 13: Exercise 1: airfoil_lift
Run a simple ‘airfoil_lift’ test case
P(1) and P(2) are two model parameters (deterministic)
V => X(1) and CL => X(2) are two random parameters for which we want to compute sensitivities.
To run ‘airfoil_lift’ case, modify ‘testSensitivity.m’ by changing caseName = ‘airfoil_lift’

## Slide 14: Output
marginal
convergence
sensitivity
CL
V
CL
V

## Slide 15: Part II Sensitivity analysis ECN AeroModule

## Slide 16: Structure
Main routine to run sensitivity analysis.
We only change variable ‘caseName’ in this routine

## Slide 17: cases
Contains different test cases; we are interested in aero_module directory

## Slide 18: aero_module
Routines containing turbine data and uncertainty description

## Slide 19: NM80.m
Has two parts:
1 . Deterministic part
extracted from “input.txt” file
2. Stochastic part to describe
probability distribution of
random parameters

## Slide 20: Adding an input parameter
Random variable should be described in UQLab format, for example, truncated Gaussian for RPM is defined as follows:

## Slide 21: Adding an input parameter
Weibull distribution for wind speed
New input parameter can be added anywhere in NM80.m as the order in not important

## Slide 22: For vector input parameters
For vector parameters, such as chord and twist, each control point is treated as a random input

## Slide 23: Parameterizations done separately

## Slide 24: Choosing parameters for SA
A list of all possible parameters
Few selected from the list

## Slide 25: aero_module
Routine for describing sensitivity analysis related options

## Slide 26: initialize.m
Turbine data filename
Four methods to compute sensitivity
Parameters for different methods

## Slide 27: aero_module.m
This routine run the AERO-module package and reads the output quantity, power and axial force
Four methods to compute Sensitivity

## Slide 28: Setting up Aero-module
Directory should have same name as the turbine
Make a copy of reference polar files

## Slide 29: Exercise 2: SA of operational parameters for Power
1. Changes in NM80.m file
2. Changes in initialize.m
3. Modify ‘testSensitivity.m’ by changing caseName = ‘aero_module’ and run it

## Slide 30: Output

## Slide 31: Output Variables
Mean and standard deviation of the quantity of interest is stored in variables: mean_LARS, std_LARS
Sobol_LARS_Total contains Sobol indices for runs with different number of samples
AVG_Sobol_LARS_Total contains averaged Sobol indices w.r.t number of repetitions (LARS_repeat). These are plotted in the histogram (see PostProcessing.m)

## Slide 32: Part III Miscellaneous topics

## Slide 33: Exercise 3: Change turbine and add uncertainty
Run SA for ‘AVATAR’ turbine
Add PITCHANGLE as a new input parameter in SA
  Truncated Gaussian distribution with mean =PITCHANGLE, Std=1, LB=-2,UB=2
Use two methods, PCE_LARS and PCE_OLS
Discuss the result and verify that SA is correct?

## Slide 34: Pending
Parameterizing a curves using B-splines, different approach for polars and chord, twist
Vector as output quantity
Adding more model parameters in the analysis